## Slide 1
Storing H2 in Aquifers using CO2 as Cushion Gas, the Thermodynamic Behavior of the System
BEN RHOUMA Sabrine – PhD candidate

## Slide 2
Introduction
Storing H2 in aquifers
Cushion gas represents 30-60% of total gas
Using H2 increases investment costs
Other cushion gases
  would mix with H2 and increase operational costs
  would react with H2 assisted by microbial activity (or other catalysers)
CO2 as cushion gas
  Environmental benefits
  Decreases investment costs
  Interesting physical properties around critical point

## Slide 3
Introduction
CO2 as cushion gas
What about H2 - CO2 mixing and reaction?
Mixing
thermodynamic behaviour of the system H2 - CO2;
Reservoir conditions and reservoir quality;
Injection and withdraw rates
Reaction (not studied here but)
Examples of methanation in situ involve other gases, not only pure CO2
Sabatier reaction occurs at high temperature (300°C to 400°C)
Uncertainty of microbial activity kinetic
CO2 - H2 system
Type III Phase Diagram
Streett et al., 1983 « Phase Equilibria in Hydrogen Binary Mixtures From 63 to 280 K and Pressures to 6000 Bars ».
Gordon,1972 « A Supercritical Phase Separation ».

## Slide 4
Interesting properties of CO2 around its critical point
Density
Derived from Equation of states;
High density contrast between CO2 and H2 at CO2 critical point and around
“Contaminants” sensitivity in pure CO2 phase
  a concentration of H2 as low as 2% could lower the density by as much as 25% compared to pure CO2 at “CCS conditions” (Sanchez-Vicente et al, 2013)
Property | Hydrogen | CO2 | CO2 critical (32°C at 73 bars)
Density (gaseous) at 0°C, 1 bar (kg/m3) | 0.089 | 1.951 | 
Density at 25° C, 100 bar (kg/m3) | 7.67 | 813.9 | 434.87
Density at 50° C, 100 bar (kg/m3) | 7.1 | 384.4 | 
Boiling point (1bar) | -252.76°C | -78,6°C | 
Viscosity at 25° C, 100 bar (µPa-s) | 9.15 | 75.29 | 35.103
Viscosity at 50° C, 100 bar (µPa-s) | 9.638 | 28.34 | 
Coefficient of compressibility at 25° C, 100 bar (Z) | 1.06 | 0.2186 | 0.37149
Coefficient of compressibility at 50° C, 100 bar (Z) | 1.056 | 0.4262 | 
Difference in physical parameters for H2 and CO2 at same P/T conditions
(data from Peace and NITS databases, 2021)
EoS capacities and limitations:
H2 % mol EoS | 2 | 7,5 | 10
GERG 2008 | 4% | 17,5% | 14%
Peng Robinson | 16% | 10,5% | 9%
SRK | 16% | 12% | 10,5%
The maximum relative error between the experimental and calculated densities using different EoS
CO2 – H2 system
Phase diagram

## Slide 5
EoS capacities and limitations:
GERG -
2008
relative error between the experimental and calculated densities using different EoS
Notes: The dot points here represent the calculated values but also the experimental ones, on x we have T and for Y pressure and the three figures are for different hydrogen mole fractions 2%, 7,5% and 10%.
we can note that for GERG the highest error is really located around “the critical point of the CO2” but with increasing pressure?

## Slide 6
EoS capacities and limitations:
PR
relative error between the experimental and calculated densities using different EoS
Notes: Whereas for the cubic EoS PR using the translation volume of peneloux ,the error is distributed over a wider range of temperature and pressure

## Slide 7
EoS capacities and limitations:
SRK
relative error between the experimental and calculated densities using different EoS
Notes: The same interpretation is applied to SRK
The choice here is between cubic EoS with average results at the overall or being more specific but with high located error,
Now besides the discussion about the different EoS, it is also valuable to discuss the phases evolution. Here we notice that the diphasic zone exhibit higher pressure for increasing hydrogen fraction

## Slide 8
thermodynamic behaviour of the system H2 - CO2
CO2 – H2 system
Phase diagram

## Slide 9
5% ≤H2 ≤ 25%
Conceptual model
16,8°C
25°C
30°C
CO2 – H2 system
Phase diagram

## Slide 10
CO2 gas mole fraction
CO2 liquid mole fraction
H2 Gas mole fraction
Scenario 1
Scenario 2
Scenario 3.2
CO2 – H2 system
Concept simulation*
* CMG-GEM courtesy
16,8°C
25°C
30°C

## Slide 11
The investigation the P-T-x diagram of the system of interest concluded the possibility of 2 phases to exist.
The examination of the different EoS is a valuable guidance towards a robust equation, in order to better describe the complex liquid –gas behavior.
A multicomponent, multiphasic module
Conclusions
Storage conditions CO2 – H2 system
27°C

## Slide 12
Conclusions
Feasibility of H2 – CO2 aquifer storage
Offshore reservoirs are promising targets to enable the concept,
Two-phase zone would serve as buffer zone limiting mixing
Challenge to simulate realistic cases
  Numerical complexity
  EoS uncertainties
Ongoing Testing
Realistic case

## Slide 13
Thank you for listening
Contact:
s.benrhouma@brgm.fr
BEN RHOUMA Sabrine